## Slide 1: Attentional Tracking in Real-Room Reverberation
S. J. Makin, A. J. Watkins and A. P. Raimond.

## Slide 2: Intro: Attending at Cocktail Parties
Typical listening situations:
  multiple sound sources
  numerous reflecting surfaces
  reflections degrade both intelligibility and segregation of sounds
Yet listeners able to selectively attend to a single source
Any detectable difference seems to help listeners track messages over time
  e.g. a filtering difference (Spieth and Webster, 1955)
Two main sources of differences:
Notes: such as the famous “cocktail party” – required sound must be selected from a mixture of multiple direct sounds and numerous reflected “images” of EACH sound
– reverb both degrades intelligibility of single sources and impairs separation of streams
in such situations…
showed that filtering EITHER target message or interfering message improved performance on task requiring selection and recognition of one of 2 simultaneous messages – and the degree of filtering was non-critical
There are 2 main sources of naturally occurring differences between signals….

## Slide 3: Intro: Attending at Cocktail Parties
Spatial position:
  Cues from spatial separation seem to aid tracking (Spieth et al., 1954; Broadbent, 1954)
  Interaural differences can be used to track (e.g. ITD, Darwin & Hukin, 1999)
  But these differences are corrupted by reverberation (Rakerd & Hartmann, 1985; Kidd et al., 2005)
Source characteristics:
  Talker-difference tracking cues (that include vocal-tract size) are very robust to reverberation (Darwin & Hukin, 2000)
So - in realistic levels of reverberation do listeners simply ignore corrupted cues from spatial position and rely on source (i.e. talker) characteristics for tracking?
Notes: A number of authors, such as… , in studies similar to that of Spieth & Webster, found…
In a study specifically designed to measure effects on auditory attention or “tracking”, D&H showed… a speech message over time
Both ITD and ILD are increasingly degraded as reverb increases
But which can also include pitch differences, prosody, and possibly other factors

## Slide 4: Experimental Paradigm
Based on Darwin & Hukin’s (1999a, b, 2000) paradigm, where listeners hear two simultaneous sentences played in a (simulated) room
target sentence
on this trial you’ll get the word to select
test words
bead
globe
you’ll also hear the sound played here
line difference
Which target word ‘belongs with’ the target sentence?
Above: colour/boldness competes with a line difference
Listeners here: talker versus room-position
Response indicates which cue they were tracking
Notes: The EP we used was…
One is designated the target sentence, which in our experiments was… there were also 2 simultaneous test words, and a ‘distractor’ sentence. Listeners are asked to attend to the target sentence and report which test word they hear as ‘belonging’ with it
Just substitute position in a room for position on the page, and talker for color, and you have our experiments
So their responses tell us which is the more influential source of cues for tracking

## Slide 5: Stimuli
BRIRs recorded in room (135 m3) using dummy heads:
sine-sweep
dummy-head talker
real-room
dummy-head listener, mics in ears
BRIR
deconvolution
Convolved with dry recordings to reproduce real-room reverberation:
convolution
headphones
real-room listening
‘dry’ speech recording
BRIR
listener
=
‘spatialised’ speech recording
Notes: Measurement signal – log-sine-sweep (Farina)
Talker – B&K HATS
Listener – KEMAR
‘virtualised’ or ‘spatialised’ ?
The listener has an experience very close to being in the room where the recordings were made – all that is missing is individualised HRTF (pinna and head) effects

## Slide 6: Stimuli
Numerous room-position pairs sampled,
varying distance separation,
listener
talkers
Probability of room response averaged across position-pairs
Presented both dichotically and diotically
Diotic stimuli were L or R channel presented to both ears, level-corrected to match dichotic stimuli
bearing difference,
or both

## Slide 7: Results: Talker Differences
Different sex
Same sex
0.2
0.4
0.6
0.8
Talker difference dominant
- especially when diotic
Diotic – talker (if anything)
Dichotic – room-position
Which cues from room-position are responsible?
room
talker
dichotic
diotic
0.2
0.4
0.6
0.8
diotic
dichotic
room-position
response probability
room-position
response probability

## Slide 8: Methods: BRIR Processing
BRIRs processed to limit available cues:
‘Spectral Only’ (SO) BRIRs
  removes ITDs and temporal-envelope ‘tails’, leaving only spectral-envelope and level info
‘Spectral-plus-Temporal’ (S+T) BRIRs
  as SO, but with temporal-envelope ‘tails’ restored
BRIR
FFT
Rotate all components to cosine phase
IFFT
Window and time-align
SO BRIR
SCN
Convolve
S+T BRIR
Notes: Take the inverse transform and window the resulting function with a short Hann window
…by flipping the polarity of a randomly selected half of the signal samples. (Schroeder 68?) – check all this!

## Slide 9: Results: Comparing BRIRs
Diotic
Dichotic
0.2
0.4
0.6
0.8
Talker-difference dominant
Less so when ‘tails’ are present
Suggests an effect of ‘tails’ is to disrupt pitch cues? (Culling et al., 1994)
Room-position much more dominant
- even without ITD cues
Is this due to ear ‘selection’?
Or inter-aural processing?
Unprocessed
SO
S+T
0.2
0.4
0.6
0.8
Unprocessed
SO
S+T
room-position
response probability
Notes: this suggests to us… because with changing F0s, as reflections arriving at different times tend to have different F0s, harmonicity gets disrupted. This would impair pitch-based tracking cues which would tend to promote “talker” responses, leading to either an increase in reliance on other, in this instance, position-based cues, or else just to a reduction in the info available leading to a “guessing” situation
So. What might be going on here? There seems to me to be 2 candidate explanations. Listeners could be ‘selecting an ear’ – or it could be due to genuine inter-aural processing.
What do I mean by this? - Let me explain by reference to the information available to listeners - The only info remaining in processed conditions is spectral and level info., so lets have a look at some IR spectra…

## Slide 10: Spectral Characteristics of BRIRs
Power (dB) in channels of an ‘auditory’ (gammatone) filterbank:
Can also compute distance between ILD profiles for each BRIR in a pair
So - is dichotic effect due to ‘selecting’ ear with biggest distance, or is it due to different ILD profiles of the room-positions?
dB
0.65 m
5 m
200
531
1117
2155
3994
7252
-70
-50
200
531
1117
2155
3994
7252
+ 25
- 25
200
531
1117
2155
3994
7252
Left ear
Right ear
0
-70
-50
10
ILD
200
531
1117
2155
3994
7252
-10
0
10
0
10
-10
0
10
0
10
Spectral distances between channels of 2 BRIRs in each position-pair
– which differ among positions
– and between ears
– which also differs widely among room positions
d = 25
d = 16.6
d = 43.5
d = 25.5
d = 43.8
d = 16.6
Notes: Here I’m plotting “auditory” spectra generated by processing the BRIRs with a gammatone filterbank (32 channs, equally spaced on ERB-rate scale between 200 – 8k) dB on ordinate, channel CF (Hz) on abscissa.
You can see that the two spectra are different. So below that I’m plotting the absolute distance between the two. And just taking the rms of these values in each channel gives us a Euclidean distance between these spectra (plot d number) – so we’ve computed a monaural spectral distance between the corresponding channels of the two BRIRs of a particular position-pair (plot text). This is at the closest distance. – But it differs amongst diff room positions… and its different for the two ears…
We can also compute an ILD profile for each BRIR position by subtracting the R channel from the L – and subtract the ILD profiles of the 2 BRIRs in a position-pair to get a distance between the 2 ILD profiles…
…and these also differ widely among different room positions…
In other words - are these MONAURAL distances associated with an increased frequency of room-p responses?

## Slide 11: Correlation with Spectral Distances
Dichotic
room-position response probability
.5
1
SO
Diotic
SO
Monaural distance does not predict listeners’ responses
The associated cues seem to be ignored
So listeners are unlikely to be ‘selecting’ an ear on this basis in dichotic conditions
Distances between ILD profiles are predictive of responses (r2 = 0.46)
So the dichotic effect appears to arise through inter-aural processing of ILD
Monaural Euclidean spectral distance (dB)
Euclidean distance between ILD profiles (dB)
20
40
60
20
40
60
r = 0.17
r = 0.68
Notes: Here I’m treating R and L versions as distinct and plotting each distinct positioning of IRs which includes cases where the near IR is on the right and far on the left, and vice versa.
And the answer is… no.
Monaural distances are only very WEAKLY correlated with the frequency of room-p responses

## Slide 12: Conclusions
When tracking speech in simultaneous messages, cues from talker differences are not always dominant
Cues from position differences can sometimes be more influential - even in reverberation
This is mostly seen when talker differences are subtle, listening is dichotic, and pitch cues are degraded
The cues from position differences are not the messages’ ITDs - they seem to be the ILDs - which still differ among positions in a typical room
This dichotic effect doesn’t seem to arise through listeners 'selecting' an ear – appears to be due to inter-aural processing

## Slide 13: Thanks for attending!